## Slide 1
Multi-Level Smart Alarm System
Professor: Ahmet Gurhanli
Team Member:
Asma Atiah – 22040102149
Shahd Atayturkmen-22040102137
Ayet Selim – 22040102159
Malak Medhat - 22040102054

## Slide 2
General Idea:
The Multi-Level Smart Alarm System (ML-SAS) is an advanced 8-bit embedded security solution powered by the DMC8 microcomputer. It is designed to provide dynamic security responses based on the user's environment through three distinct operating levels:
Normal/Home Mode: Monitors basic security parameters with visual status feedback.
Travel/Vacation Mode: Enhances sensitivity and activates presence simulation to protect the premises during long absences.
Emergency Mode: A high-priority interrupt state for immediate threat response with synchronized audio-visual alarms.

## Slide 3: Input Ports:
IA0 (Emergency): High-priority trigger for immediate danger.
IA1 (Travel1 Mode): Activates the long-term absence protection logic.
IA2-IA5:(SecCODE) The 4-bit hardware interface for the security passcode (14h).
IA7 (Silent Mode): Toggles between audible alarms and discrete notifications.

## Slide 4: IA0: Emergency Button

## Slide 5: 2. IA1: Travel Mode Explanation

## Slide 6: 2. IA2–IA5: Security Code (SecCODE)

## Slide 7: 3. IA7: Silent Mode

## Slide 8: 4. Data Acquisition:

## Slide 9: Output Ports:
OA2 (Green LED): Indicates the Safe State; the system is powered on and no intrusion or emergency is detected.
OA1 (Red LED): High-visibility Emergency Alert; flashes or stays on to signal immediate danger or a panic trigger.
OA3 (Yellow LED): Indicates Travel/Security Mode; the system is in a high-sensitivity state for long-term protection.
OA0 (Blue LED): Silent Alarm Indicator; provides a visual-only notification when the audible buzzer is toggled off via Silent Mode.
OA7 (Audible Buzzer): Provides the Acoustic Warning; sounds during Emergency or Security breaches to alert the surroundings.

## Slide 10: 1. Visual Feedback Green LED (Safe State):

## Slide 11: 2. Visual Feedback Red LED (Emergency Alert):

## Slide 12: 3. Visual Feedback Yellow LED (Security/Travel Mode):

## Slide 13: 4. Visual Feedback: Blue LED (Silent Alarm)

## Slide 14: 5. Audio Output: The Buzzer

## Slide 15: 6. Serial Data Output: ASCII Status (Port OD)

## Slide 16: Serial Communication (Remote Interface):
ASTX (Serial Transmitter): Responsible for sending system status data to a remote terminal. It converts the 8-bit parallel data from the OD Port into a serial bitstream.
ASRX (Serial Receiver): Responsible for receiving incoming serial data. In this system, it can be used to monitor the status characters ('G', 'E', 'S') sent by the controller.
RDY Signal (Handshaking): A feedback signal from the transmitter to the CPU (connected to ID0). It tells the processor to wait until the transmitter is ready to send the next character, preventing data loss.

## Slide 17: Serial Communication (Remote Interface) 2:
Status Codes (ASCII): The system transmits specific letters to represent the current state:
  'G' (47h)(01000111): System is Good/Safe.
  'E' (45h)(01000101): Emergency alert detected.
  'S' (53h)(01010011): Security/Travel mode active.

## Slide 18: State Machine Logic (Decision Making)
The system doesn't just run line by line; it "decides" which mode to enter based on input priority:
Bit Testing: The CPU uses the BIT instruction to constantly poll (check) the status of the input pins.
Conditional Jumping: Depending on the results, the system uses JP NZ (Jump if Not Zero) to switch states:
  Normal Path: Stays in a loop checking for activity.
  Emergency Path: Overrides all functions if IA0 is triggered.
  Security Path: Enters the monitoring state if IA1 is active.

## Slide 19: The Security Protocol (The Digital Lock)
Explain how the system verifies the user’s identity before disarming the alarm:
Input Isolation (AND Masking): To read the passcode from IA2–IA5, the CPU uses AND 3Ch. This ignores all other switches and only focuses on the 4-bit code.
Comparison Logic (CP Instruction): The instruction CP 14h compares the user’s input directly with the hardcoded secret value (14h).
Validation: * If the result is a match (Zero Flag set), the system jumps to START to reset the alarm.
  If the result is wrong, it remains in the CHECK_AGAIN loop, keeping the alarm active.

## Slide 20: Multi-State Monitoring: Offers four distinct operational modes: Safe, Emergency, Security (Travel), and Silent, each with unique visual and audible indicators. Secure Passcode Verification: Implements a digital lock mechanism that requires a specific 4-bit passcode (14h), verified through bitwise AND masking and logical comparison. Dual-Layer Alert System: Combines visual notifications via multi-colored LEDs with an audible Siren (Buzzer) for comprehensive user alerting. Selective Alerting (Silent Mode): Features a dedicated Silent Alarm (Blue LED) that can be toggled via hardware switch (IA7) to provide discrete notifications without sounding the buzzer. Real-Time Status Reporting: Utilizes Serial Communication (TX/RX) to transmit ASCII status codes ('G', 'E', 'S') for remote monitoring and system tracking. Reliable Hardware Handshaking: Integrates a RDY signal to synchronize the CPU with the transmission module, preventing data loss during communication.
System Key Features: